## Slide 1
SRM:
A solid rocket motor (SRM) is a device that propels a rocket forward by burning a solid fuel mixture and releasing the resulting exhaust gases.
DRDO : A Solid Rocket Motor Design & Safety
By: Jishnu Teja Dandamudi , Sarvesh Ram Kumar
Existing Issues: Vulcan rocket: In October 2024, the nozzle extension of a solid rocket motor on the second flight of the Vulcan rocket failed. The failure occurred 23 seconds into the flight.The failure was similar to 2019 failure of Omega GA rocket booster test. H-IIA rocket: The H-IIA rocket's solid rocket boosters had a greater than expected ablation of nozzle Insulation. After five ground tests, the H-IIA F1 was launched successfully.
Link for the prototype created by us using a small dataset: https://github.com/Sarvesh-Ram-Kumar/Solid-Rocket-Motor-Safety-Prediction

## Slide 2
Development of ML/AI module for rocket motor design:
  Solid Rocket Motor : Long-term storage .
  The Solid Propellant grain : Particulate composite (viscoelastic) material.
  Mechanical behavior : Time-temperature dependent on loading condition.
  The Major loads : Thermal cycle , operating Chamber pressure.
  The Failure modes : Surface crack, particle cracking, de-wetting, propellant tearing,de-bonding at propellant & insulation interface.
  Predict : Margin of safety of Solid Rocket Motor with time

## Slide 3: The Main Issues
Ageing of the Rocket
Chemical Changes in Propellant Grain
Cracks in the Insulation Material
Type of Fuel, Oxidizer and Insulation material used
Loss of Adhesion in propellant-particles
Storage Conditions and Environment
Irreversible Process and causes trouble in ignition
Pressure Indifferences
Causing engine damage and disruption in combustion chamber
Carbon-fibre insulated SRMs have longer lifetime
Maintaining the temperature and humidity is important.
If Not
Done

## Slide 4: Methodology in Python
Import Libraries:
Numpy , pandas
Import The Dataset
Encode the Data
Train the Model using Ensemble Library
Predict New Results
Used for Reading Dataset
Numpy for Operations
Using ILOC method
Has both Numerical and Categorical
Using One Hot Encoder and Column Transformer
Categorical Data : Insulation :
Strong – ( 0.0 , 1.0 , 0.0 )
Weak – ( 0.0 , 0.0 , 1.0 )
Medium – ( 1.0 , 0.0 , 0.0 )
By Giving test cases with Insulation Material and Age of SRM

## Slide 5: Using Random Forest Regression Technique
Age of the Propellant
Insulation Material
Train the Model
Shear Strength
Give test cases with
Age of the Propellant
Insulation Material
Output : Shear Strength
Dependable Variable
No of Decision Trees Used=10
Ensemble Learning
Model Trained
Ensemble leaning is a ML concept which combines multiple models to give better accuracy.
And More Features